## Slide 1
PROBLEM STATEMENT
Assessing outage impact querys with an agentic system
What if these cells
go offline?
carrier · sector · site
agentic
system
LLM, Tool boxes, Skill libraries, Dataset
Traffic redistribution which backup cells
Impact map loss · degraded · ok
Affected region types residential · highway · commercial
Outage assessment enables planned shutdown and resilience analysis
Planned shutdown -> minimize impact, notify customers ahead
What-if assumption for every site -> locate vulnerable parts of the network

## Slide 2
Challenges For Outage Analysis
The task itself is multi-source with an unbounded investigation space.
No single source suffices
coverage, KPIs, and geography must be examined jointly
Coverage
KPIs
OpenStreetMap
Population
→ jointly
The path cannot be pre-defined
each finding changes where to look next
fixed pipeline
Step 1
Step 2
Step 3
evidence-driven
Check coverage
Expand along highway
Inspect backup KPIs
Only an agentic system is both scalable and comprehensive
Manual
Existing tools
Agentic system
Multi-source evidence
✓
✗
✓
Multi-granularity (carrier · site · cluster)
✓
✗
✓
Adaptive investigation
✓
✗
✓
Automated & scalable
✗
✓
✓

## Slide 3
Challenges for Agentic Outage Analysis
The agent must decide what to investigate next and which actions to take
based on partial evidence.
The agent must determine when the available evidence is sufficient
to stop the investigation.
During offline learning, the system must identify which steps caused
a trace to fail and why.
A verification agent must check the validity of each step and whether
the evidence supports its conclusions.
Notes: Open challenges for the proposed cellular outage analysis agent. The investigation policy must choose both the next goal and an action given partial evidence. Stopping criteria must distinguish sufficient evidence from exhaustion of the available budget. Offline failure diagnosis must locate the steps or decisions responsible for an unsuccessful trace. The verification agent and its criteria remain to be designed. It should check intermediate steps and the evidence behind their conclusions. These are design requirements, not claims that verification guarantees correctness.

## Slide 4
Offline investigation loop
01
Executor agent
Skill library
Planning
Functional
Atomic
What-if query
Cell ID
Outage time window
Investigation Context
Evidence with sources
Query Coverage
Choose the next
investigation goal
LLM identifies what
to learn next
Choose the next action
using retrieved skills
LLM selects tools from skill steps
Tool library
Query OSM
Geographic features
Query coverage
Per-location cell coverage
Query KPIs
Historical RRC, PRB, Volume,…
Estimate redistributed load
Demand and allocation model
Planning guidance
Procedures and tool usage
Goal
Action
Geographic features/coverage/historical KPIs/load estimates
End-to-end execution traces
Goals, actions, results and errors
Skill refinement (Fig. 2)
Updates the shared skill library
Offline feedback
(eg. learn the surrounding lanuse)
Recent actions and observations

## Slide 5
Offline skill extraction and refinement
02
Original manual trace
Query, actions and results
Reasons for each step
Conditions and assumptions
Tool specifications
Inputs, outputs, constraints
Available tool interfaces
LLM skill extraction
Generalize task steps
Retain conditions and branches
Parameterize inputs
Skill library
Planning
Goal selection
Conditions, priorities and branches
Example: rural cell→ wider initial scope
Functional
Task execution
Inputs, outputs and tool workflows
Example: identify activity regions
Atomic
Tool use
Arguments and constraints for each single Tool
Example: OSM query API and parameters
Each skill retains its source trace and applicability.
Offline investigation (Fig. 1)
Use the library in the next rollout
Record goals, actions, observations and errors
LLM skill refinement
Extract reusable experience
Merge or revise skill entries
Check tool-schema compatibility
Original Skills
Retrieve applicable skills
Execution trace
and tool feedback
Add, revise or merge

## Slide 6
Challenges for agentic outage analysis system design
Challenge | Design question | Candidate approaches
1 Adaptive action selection | How does the agent choose best action from partial evidence? | Context engineering and action interface design (MCP server/ tool library design)
2 Investigation stopping | When can the system accept a request to end investigation? | Completion checks and independent validation sampling ()
3 Decision error detection | How can the system detect incorrect investigation judgments? | Targeted verification queries and expert feedback
4 Correction and recovery | How can the system correct a decision and resume execution? | State correction, checkpointing and selective re-execution
5 Experience across cases | How can verified experience improve future investigations? | Case retrieval, in-context learning and validated skill updates
Candidate approaches for discussion. Initial PoC scope to be confirmed.
Notes: Scope
These are candidate design directions for discussion, not implemented mechanisms or demonstrated contributions. The agent performs spatial investigation before final backup and load calculations. Existing tool interfaces and calculation capabilities remain baseline infrastructure.
Adaptive action selection
The LLM chooses the next action. Context organization and action interfaces are separate choices that can be compared while holding the model, tools, data and stopping policy fixed.
Investigation stopping
Completion checks establish compliance with a declared investigation protocol. Independent sampling can find omissions within its scope, but it does not establish exhaustive coverage. Budget exhaustion and missing required evidence return an incomplete status.
Decision error detection
Focus on valid tool calls followed by unsupported or incorrect investigation judgments. For example, roadside observations alone do not establish the absence of target-cell coverage throughout a residential area. Targeted verification may refute such a claim. A different next action or an expansion justified by new evidence is not automatically an error. Some judgments require expert feedback.
Correction and recovery
Correct the affected state and repeat the required work. Retain observations that remain valid. A checkpoint enables recovery, but does not identify errors or determine the correct repair. Compare recovery methods using the same identified error and correct feedback.
Experience across cases
Case retrieval and in-context learning reuse existing experience at inference time without updating model weights. An offline process can propose skill changes, evaluate them on validation cases, and accept or reject them. Keep final test cases separate from candidate selection. This remains a candidate extension until feedback and evaluation data are available.
Method references
ReAct: https://arxiv.org/abs/2210.03629
SWE-agent: https://arxiv.org/html/2405.15793v3
LangGraph conditional routing: https://docs.langchain.com/oss/python/langgraph/graph-api
LangGraph persistence: https://docs.langchain.com/oss/python/langgraph/persistence
LangGraph interrupts: https://docs.langchain.com/oss/python/langgraph/interrupts
LangGraph time travel: https://docs.langchain.com/oss/python/langgraph/use-time-travel
Reflexion: https://arxiv.org/abs/2303.11366