## Slide 1
What Is Built: Buying Down Uncertainty
The answer is never computed once — it starts as a wide range, and every query exists to narrow it.
RRC_loss = B × ( H + O ) each variable held as [low, mid, high] — bounds on its true value
B Baseline connections
How many RRC connections the cell actually carries in that window.
narrowed by: Snowflake KPI query (historical same-window)
prior
after query
H Coverage-hole share
How much of the area is left with no usable neighbor signal — those users drop.
narrowed by: Coverage API: coarse scan, then targeted refine
prior
after query
O Overload share
How much has coverage but cannot be absorbed — neighbors near capacity.
narrowed by: Neighbor-load KPIs over the confirmed neighbor set
prior
after query
In what order? score = U(v) × r ÷ c — narrow whichever variable buys the most certainty per unit of query cost. When to stop? max score < θ: nothing left is worth its price. Budget hard-capped in the tool layer; every step logged with evidence.
Notes: One story, top to bottom: the answer is an interval; its width comes from three variables; each variable has its own data source that narrows it; the order of narrowing is chosen by certainty-per-cost; we stop when nothing is worth its price. Built and running: KPI registry + parameterized SQL behind B and O, coverage scan/refine behind H, LangGraph loop with milestones, judge, evidence provenance and checkpoints around it all.

## Slide 2
Not Done Yet: Two Designed Extensions
Both fully specified, awaiting implementation — neither blocks the current RRC deliverable.
Throughput chain
T_loss = T × ( H + (1−H) × L ), L = 1 − s × p
T = baseline traffic — same Snowflake query as B, extra columns only
H is shared with the RRC chain — one coverage scan feeds both
s = spectral-efficiency retention from ΔRSRP (dominant vs 2nd-best) — already a by-product of coverage evidence
p = PRB-availability retention from neighbor load — already collected for M4
Work items: monotone-direction support in propagation, M1/M5 contract + rubric extension
Bounded worker autonomy (kpi_analyst first)
plan params → execute → self-check (max 2 internal retries)
Why: a 0-rows neighbor query (site-ID format mismatch) was silently recorded — nobody owned the judgment “this result is wrong”
LLM freedom = one validated JSON of query params within the 2D data contract — still no SQL, budget untouched
Self-check is rules first: entity coverage (rows per requested ID), value-range sanity from the KPI registry
On failure, LLM picks from a fixed menu: submit_partial / retry_with_mapping / retry_lower_granularity / report_anomaly
Output is a proposal — deterministic update_chain validates it before anything touches the intervals
Both reuse evidence the system already collects — the marginal cost is engineering, not query budget.
Notes: Two extensions, one message each. Throughput: the formula is ready and almost all of its inputs are by-products of data we already buy for RRC. Worker autonomy: motivated by a real incident; the autonomy is enum-constrained and proposal-based, so auditability is unchanged.