## Slide 1
USID Outage Impact Assessment
Presenter: Xinyue Zheng
Collaborator:

## Slide 2
Problem: Assessing the Impact of Cellular Base Station Outages
Scenario:
A cellular base station goes offline (maintenance or failure)
Q1
How severe is the impact?
Customer care calls increase significantly
Q2
Where does the impact occur?
Which geographic zones are most affected?
→ Accurate pre-assessment enables proactive planning and resource allocation
OFFLINE
Affected users
Unaffected users
Tower
PROBLEM FORMULATION — HOW WE MODEL IT
INPUT — Multimodal feature data
Temporal
KPI
Per-USID KPI data
Historical throughput & volume · Hourly traffic profiles
Spatial
Rhea
Geospatial signal measurements
RSRP, SINR, RSRQ at each geographic coordinate · Coverage across service area
Static
ATTR
USID static attributes
Physical & spectrum attributes · tower height, 4G/5G, …
· · · extensible to additional modalities
→
LABEL — Operational proxy
Customer care calls
volume · Δ increment
during & post outage window
OUTPUT — Severity level
L1
L2
L3
L4
L5
5-class · boundaries defined by domain knowledge

## Slide 3
Limitations with Manual Expert Assessment
Scale
Thousands of base stations
Parallel assessments required
Engineers become bottleneck
Speed
Fast turnaround required
Manual analysis takes hours
Missed scheduling windows
Traceability
Reasoning not recorded
Hard to reproduce decisions
Weak post-incident audit
Manual expertise is effective, but not scalable, fast, or auditable

## Slide 4
From Manual to Autonomous
How should we automate the assessment? Three natural approaches:
①
Train a
specialized model
✗
Requires large labelled dataset (thousands to hundreds of thousands)
✗
Poor generalization to new tasks
✗
Low interpretability, fully black-box
②
Fine-tune
a large LLM
✗
Expensive and time-consuming to adapt
✗
Requires domain-specific labelled data (hundreds to thousands)
✗
Limited control over reasoning process，still remains data-driven
③
Off-the-shelf
LLM agents
✓
Can leverage few-shot examples without retraining.
✓
Prompt- and rule-driven reasoning offers traceability
✓
Domain rules explicitly injected via prompts → behavior stays aligned with expert knowledge
✓
Modular and easily adaptable
Our approach
We shift from data-driven prediction to structured, rule-guided reasoning

## Slide 5
Single Agent vs Multi-agents
Single-agent struggles with…
✗
Context overload
All modalities handled in a single prompt → degraded reasoning
✗
Lack of specialization
Different sub-tasks hard to optimized via one agent jointly
✗
No intermediate verification
No mechanism to check reasoning during the process
→
Multi-agent enables…
✓
Decomposed context
Each agent operates on a focused subset of information
✓
Specialized reasoning
Each agent focuses on one aspect
✓
Enables structured verification
Per-agent checks + cross-agent validation become possible and keeps consistency
Decomposing the problem by modality enables both better reasoning and stronger auditability

## Slide 6
How to make the most of Agents
Prompt Engineering
Tell the model what to do
Context Engineering
Give the model the right information
Harness Engineering
Control how the system executes
Enable reliable multi-step workflows
"The bottleneck shifts from input design to execution control"

## Slide 7
What is Harness Engineering?
"Harness Engineering is the design of the execution system around an LLM"
Agent + Harness = whole system
Not just providing information, but controlling execution
Orchestration
Predefined workflows
Dependency management across steps
Execution Modules
Specialized agents or tools
Each handles a specific subtask
Verification & Control
Validation and evaluation
Error detection and correction
State & Memory
Intermediate results
Persistent storage (e.g., logs or memory systems)
"A harness turns an LLM into a reliable system"

## Slide 8
System overview
Input prompt
Prompt parser
Harness
Orchestrate & dispatch agents
Enforce verification & rerun logic
Coverage & load agent
Attribute analysis agent
KPI analysis agent
Geo-correlation agent
Final assessment agent
Analysis agents
Cross agent verifier
Reflector
agent
Output result
Run-store MCP server
Ruess-memory MCP server
preprocess
Verification & reflection agents
: Per-agent verification agent
: work-flow
data exchange via MCP
data exchange via MCP

## Slide 9
Harness
Trigger preprocess; input USID, shutdown window
Numeric facts
Computes every numeric fact about signal quality, coverage, and KPI pattern— pure Python, no AI, fully auditable.
Preprocess
Fetch Raw data via MCP server
Run-store MCP server
Preprocessing
Dominance map
SINR heat map
RSRP coverage map
Statistics fact of USIDs’ signal quality, coverage file
USIDs’ KPI pattern file
Signal map artifacts
processed data stored
Compute stats and maps
Store via MCP server
Raw Data: Rhea raw data, KPI data, USID attribute
databases

## Slide 10
Analysis Agent Architecture — Shared Pattern
All analysis agents share the same execution pattern — only inputs, task focus, and outputs differ
analysis result
Rules Memory MCP
domain rules
Learned lessons
RunStore MCP
fetch input
Store analyses file
read / write
Each analysis agent receives an analysis skill.md injected by harness:
How to query input data
How to query domain rules
Task definition
Reasoning format
Checking agent verifies based on check skill.md:
reasoning chain self-consistency
rule application correctness
conclusion matches evidence
Harness:
Trigger the Analysis agent
Pass → proceed to next step
Fail → force rerun (≤ 2×)
Persistent fail → escalate to human
Checking agent
Analysis agent
Fail/Pass

## Slide 11
Multi-Perspective Analysis Agents
Different agents plug into the same harness to analyse risk from complementary dimensions
Coverage
& Load
INPUT
RSRP, SINR, coverage maps, signal stats file
TASK
Can backup cells absorb redistributed users without overload?
OUTPUT
Per-backup overload risk & load redistribution verdict
Attribute
INPUT
Statistics fact file
TASK
Evaluate each backup cell's hardware capacity & flag 5G downgrade risk
OUTPUT
Downgrade risk & capacity description
KPI
INPUT
USIDs' KPI pattern file
TASK
Forecast hourly traffic load during shutdown & identify saturation and peak-collision risks
OUTPUT
Saturation risk & peak-collision risk
Geo
Correlation
INPUT
All maps (incl. real map) + upstream results
TASK
Divide coverage area into geographic zones and assign impact severity by signal & land use
OUTPUT
Zone-level severity
Final
Assessment
INPUT
All files from previous steps
TASK
Synthesise all evidence to determine overall outage severity
OUTPUT
Overall severity level
All agents plug into the same harness with domain-specific reasoning — verification pattern identical across all

## Slide 12
Cross-Agent Verifier
Verifies that all agent verdicts are mutually consistent — conflicts are detected and resolved before final assessment
Harness
trigger after all agents pass
3cross-checks defined by domain knowledge
1
Consistency between load analysis and traffic forecast
2
Consistency between signal coverage and hardware capacity
4
Alignment between geographic severity and network risk
read all
analysis files
save verification
result
RunStore MCP
Rules Memory MCP
Domain knowledge rules & learned lessons
Conflict resolution logic from harness
Minor conflict → apply priority rules from domain knowledge then continue Major conflict → rerun both agents
Fetch all analysis files
Store verification file

## Slide 13
Reflector
Distils lessons from each verified run · appends to warm tier for future agents to learn from · only runs after full PASS
Harness
trigger only after full PASS
Looks for
Edge cases near thresholds in rules
Rules applied ambiguously or inconsistently across runs
Coverage vs KPI divergence patterns
KPI forecast modeling judgment calls
Geo zone severity close calls
append-only · no overwrite · stays silent if no new lessons
read all
findings
RunStore MCP
all agent findings
+ verifier results
append new
lessons
Rules Memory MCP
Learned lesson
(append-only)
Why this matters
Lessons accumulate across runs — future agents benefit from past edge cases without retraining. The system improves through experience, not gradient updates.